## Slide 1
Technical Guide
May. 2012

## Slide 2: xPrintServer Network Edition:As small as an iPhone
Lantronix-branded (slightly raised)
With “x” that glows Lantronix orange
Clean, elegant form factor
SIMPLE to connect, use and monitor
External (universal) power supply
Red / green LEDs for RJ45 jack

## Slide 3: Technical Overview
1. xPrintServer supports DHCP
Connect anywhere to your network (auto discovers / provisions printers on the subnet)*
* For best performance, we recommend one (1) xPrintServer for every 7-10 printers on each subnet
2. After connecting xPrintServer
to the network, xPrintServer will
get IP address from DHCP server
3. xPrintServer queries your
network printers using SNMP
4. Discovered printers are
added to the printer list
5. xPrintServer connects to the
Internet to retrieve printer
drivers

## Slide 4: Troubleshooting Guide

## Slide 5: I can’t find my xPrintServer!!
      URL: “xprintserver.local” doesn’t work!
Bonjour port is disabled within network
Check the DHCP table from the DHCP server
go to www.lantronix.com/findmyxprintserver
  Enter in serial number and we’ll discover your xPrintServer!

## Slide 6: Printer in the Printer List why cannot print??
Test page not succeeded?
IOS device report errors after sending print?
Answer: Even the printer list in the printer List, it doesn’t means the printer driver is being loaded into XprintServer!! Or loaded a wrong driver!!
xPrintServer can’t retrieve drivers
  Check Internet access (outbound port 80)
  Outbound connections blocked

## Slide 7: Auto Discovery – Wrong Printer Driver Loaded

## Slide 8: Manually Add Printer – Select the right Printer Driver

## Slide 9: Add Printer – Discovered / other Printer Protocol

## Slide 10: Select the right printer driver

## Slide 11: If your iOS device doesn’t see provisioned printers:
  It may be blocked by firewalls
  Open port UDP 5353 (bonjour port)
Check Multicast setting within the routers

## Slide 12: Air Print Requirement – Router Sonic Wall –SonicOS

## Slide 16: Still No Hope??
Send Diagnostic In formation to our support team.

## Slide 17
Don’t see your printer listed?
  Request to add your printer
  http://www.lantronix.com/info/xprintserver/add-my-printer/

## Slide 18: FW version 1.1.0-64 to 1.1.0-71
KNOWN ISSUES
==========
1) Using the Print Test Page action in the Printers menu may fail for high resolution printers.
2) Downgrading from a Beta version to a Production version of firmware may cause device
configuration to be lost.
3) xPS Release 1.1.0 will support Firmware downgrade from any installed None Production builds
(Internal167 and Beta761) to what is currently running as the latest on the xPS Production
Firmware Web Site.
Downgrading from a Beta version to a Production version requires the browsers cache to be cleared
If the xPrintServer has firmware 1.0.0-64 loaded, the updated version information reported by Check Firmware Update process is shown incorrectly (it shows 1.0.0-64). Continue with the upgrade procedure and the unit will be upgraded to 1.1.0-R71
Release Note Link:
http://ltxfaq.custhelp.com/app/answers/detail/a_id/1724